## Slide 1: Bluetooth Low Energy (BLE)

## Slide 2: Bluetooth “classic”
The “conventional” Bluetooth
2.4GHz
Range: 1m - 100m (10m typical)
Connection-oriented: audio, file transfer, networking
Reasonably fast data rate: 2.1 Mbps
Power consumption:
  < Wifi < 3G

## Slide 3: Bluetooth Low Energy
"Bluetooth Smart“
Light-weight subset of classic Bluetooth
  Operates in same freq. Range
  introduced as part of the Bluetooth 4.0 core specification
Started by Nokia as an in-house project called “Wibree”
Target Apps:
  Wireless battery-powered sensors eg. heart rate, thermometer, wearables
  Low bandwith
  No always on, constrained devices

## Slide 4: BLE Applications

## Slide 5: Bluetooth Classifications
Bluetooth Classic
  high throughput, e.g. wireless audio and file transmission.
Bluetooth Smart
  State information
  Devices with low-duty cycles
Bluetooth SmartReady
  These devices are essentially the “hub” devices such as computers, smartphones, etc. They support both the “classic” and “smart” devices, just as our smartphones can connect to a Bluetooth speaker to transmit audio and also communicate to a fitness tracker.

## Slide 6: Bluetooth family

## Slide 7: Wireless Technologies Comparison

## Slide 8: BLE vs Classic
Bluetooth and Bluetooth Low Energy are used for different purposes
Bluetooth Classic
  can handle a lot of data
  consumes battery quickly
BLE
  used for applications that do not need to exchange large amounts of data
  cheap
  Marginally further range

## Slide 9: BLE Platform Support
Bluetooth 4.0 + (and Bluetooth Low Energy) is available on most major platforms:
  iOS5+
  Android 4.3+
  Apple OS X 10.6+
  Windows 8 +
  GNU/Linux Vanilla BlueZ 4.93+

## Slide 10: GAP and GAT for BLE
Generic Access Profile (GAP) or Advertising
  Information advertised to central before connection
  Name of peripheral
  Is it connectable?
  Supported features (services)
Generic Attribute Profile (GATT)
  How to exchange data once connected
  Identifies Services, Characteristics and Descriptors

## Slide 11: Generic Access Profile (GAP)
GAP responsible for “device visibility.”
Determines how two devices can (or can't) interact with each other.

## Slide 12: GAP Device Roles
GAP defines 2 roles for devices:
  Central
  Peripheral
Peripheral devices are small, low power, resource constrained devices
  Connect to a powerful central device.
Central devices are usually far more processing power and memory.
  Tablet, Mobile phone, laptop

## Slide 13: GAP - Advertising and Scan Response Data
2 ways for a device to advertise with GAP
  Advertising Data payload
  Scan Response payload.
Advertising data payload is mandatory
Scan response payload is optional
  allows device designers to fit more information in the advertising payload such a strings for a device name, etc.
Advertising Process

## Slide 14: Advertising process
Peripheral sets a specific advertising interval and transmit advertising packet
  longer delays saves power but less responsive
A listening device interested in the scan response payload can optionally request the scan response payload, and the peripheral will respond with the additional data.

## Slide 15: Broadcast Network Topology
Some devices/apps only require advertise data.
  E.g. app requires peripheral to send data to more than one device at a time.
Can include small amount of custom data in 31 byte advertising or scan response payloads.
In this way, BLE peripheral can send data one-way to any devices in listening range

## Slide 16: Bluetooth Connection
Establishing a connection between a peripheral and a central device results in 1 to 1 communiction
  the advertising process will stop
  no longer be able to send advertising packets
Communiction in both directions
Must use GATT services and characteristics to communicate

## Slide 17: Generic Attribute Profile - GATT
Defines the way that two Bluetooth Low Energy devices transfer data back and forth
Uses Services and Characteristics.
With GATT, a BLE peripheral can only be connected to one central device (e.g. a mobile phone, etc.)

## Slide 18: BLE Network Topology
A peripheral can only be connected to one central device
Ccommunication is 2 -way
Central device can be connected to multiple peripherals.
If data needs to be exchanged between two peripherals, a custom messaging system will need to be implemented
  all messages pass through the central device.

## Slide 19: GATT transactions
Follows a (strange) client server relationship
Peripheral is known as the GATT Server
The GATT Client (the phone/tablet), which sends requests to this server.
Follows master/slave approach
  All transactions are started by the master device, the GATT Client
  GATT client receives response from the slave device, the GATT Server.
Peripheral will suggest a 'Connection Interval' to the central device, and the central device will try to reconnect every connection interval to see if any new data is available,

## Slide 20: GATT Transactions

## Slide 21: GATT – Services and Characteristics
GATT transactions are based on Profiles, Services and Characteristics

## Slide 22: GATT Profile
A pre-defined collection of Services that has been compiled by either the Bluetooth Special Interest Group or by the peripheral designers.
  E.g. The Heart Rate Profile
  combines the Heart Rate Service and the Device Information Service.
Complete list of GATT-based profiles can be found here: Profiles Overview

## Slide 23: GATT Services
Breaks data up into logic entities
Contain one or more characteristics
Each service distinguished by unique numeric ID called a UUID
  16 bit
Set of officially adopted BLE services can be seen on the Services
E.g. official Heart rate service
  service has a 16-bit UUID of 0x180D
  contains up to 3 characteristic
    Heart Rate Measurement, Body Sensor Location and Heart Rate Control Point.

## Slide 24: GATT Characteristics
Represents a single data point
Similarly to Services, each Characteristic distinguishes itself via a pre-defined UUID
  Also use standard characteristics defined by the Bluetooth SIG
E.G Heart Rate:
  the Heart Rate Measurement characteristic is mandatory for the Heart Rate Service
  Heart rate measurement has UUID of 0x2A37
If you write apps that use BLE, characteristics are what you will be after with your BLE peripheral

## Slide 25: Sources
https://learn.adafruit.com/introduction-to-bluetooth-low-energy/gatt
https://www.bluetooth.com/specifications