## Slide 1: IoT Link Layer Protocols
Frank Walsh

## Slide 2: Link Protocols
Focusing down here.
Summerise IoT applicable protocols.

## Slide 3: Protocols of note for IoT at link Layer

## Slide 4: Power Line Communication (PLC)
Origins in 1950s
  remote lighting of street lights. 100 Hz and 1 kHz signals over electrical wires.
Uses existing electrical wiring to carry both data and electric power
Applicable to
  Internet access
  Utility management
  Home automation
  IoT

## Slide 5: Evolution

## Slide 6: HomePlug
HomePlug 1.0
  provides a peak PHY-rate of 14 Mbit/s. Replaced by HomePlug AV
HomePlug AV/AV2
  AV has sufficient bandwidth for applications such as HDTV and VoIP. Peak data rate of 200 Mbit/s at the physical layer. AV2 achieves gigabit-class PHY-rate
HomePlug GP
  HomePlug Green PHY specification is a subset of HomePlug AV. Intended for smart grid. Peak data rates of 10 Mbit/s
  Designed for home appliances and plug-in electric vehicles

## Slide 7: HomePlug
1.8 – 30 MHz spectrum.
Uses Orthogonal Frequency Division Multiplexing (OFDM)
Robust:
  Same information transmitted on 2-5 subcarriers
  Uses low-bit rate modulation (more resilient to High Freq. noise)
Devices form an AV logic Network (AVLN)
  Share a 128 bit AES key
  Each AVLN has central coordinator
Transmission over 2 lines (live and neutral)

## Slide 8: Security
AVLN Netork Membership Key
  All devices have default NMK
  Users/developers can configure devices to specific NMK
Using NMK, device can request an encryption key

## Slide 9: HomePlug AV2
Compatible with AV and GP
In addition
  Additional spectrum
  MIMO(Multiple Input Multiple Output): two wires with three wire combinations(line-neutral, line-ground, neutral-ground)
  Lower overhead: shorter packet
  Repeating: intermediate devices can demodulate-remodulate
  Better encoding
  Power efficient: Stations can declare sleep periods

## Slide 10: HomePlug GreenPHY
Deigned for home area networks
Monitoring and control apps
  Hence lower power, lower data rates, lower cost
Embedded in Smart Home devices:
  smart appliances
  programmable communicating thermostats (PCTs)
  electric meters
  plug-in electric vehicles (PEVs)
Audi, BMW, Daimler, Ford Motor Company, General Motors, Porsche and Volkswagen use HomePlug Green PHY specification for PEVs.
  a common, recognized standard to reduce the build complexity for suppliers and infrastructure providers.

## Slide 11: HomePlug GreenPHY
Complies with IEEE 1901-2010 (powerline networks)
Compatible with AV and AV2
Up to 10Mbps
Uses 75% less power than HomePlug AV
Version 1.1 has specific features for Evs
  Secure billing at public chargers

## Slide 12: Convergent Digital Home - IEEE 1905
defines a network enabler for home networking
Combines WiFi, HomePlug, Ethernet, Multimedia over coax(MoCA) at home
Makes home look like single network
Devices can aggregate data through multiple interfaces
  Also allows fallback on link failure
Convergent layer used to exchange Control Message Data Units(CMDU)
No changes to underlying tech.

## Slide 13: IEEE 1905.1 Management
Compliant devices use Abstraction Layer Management Entity (ALME) (protocol)
  Neighbour discovery
  Topology exchange/change notifications
  Flow forwarding rules
  Security associations
Common Topology
  Homeplug as backbone for WiFi

## Slide 14: IEEE 1905.1 Security
Push button
Press button on new and existing device
Passphrase/key in new device
NFC: User touches new device with NFC device which is existing member
Auto Config:
New access points can request configuration from existing APs.