## Slide 1: Low Power Wide Area Networks (LPWAN)
Frank Walsh

## Slide 2: What’s LPWAN
wireless telecommunication wide area network designed to allow long range communications.
Significant characteristics
  Low power
  Low bit rate
  Wide Area

## Slide 3: Why LPWAN
Useful for independent devices
Access to remote locations
Suitable for physically, energy, and computationally constrained devices
Suited to IoT!

## Slide 4: Why LPWAN for IoT
IoT devices deployed in “the field”
  Direct access without gateways etc.
  Simpler with reduced cost
Short range wireless (Zigbee, Bluetooth etc.) requires infrastuture set up:
  Firewalls, gateways, NAT etc.

## Slide 5: LPWAN usage
100s of bits/second.
Multimedia
Documents
Sensor data
Location data
Machine 2 Machine data

## Slide 6: LPWAN and IoT
Some use cases not suitable for standard wireless tech
Can provide back-up connectivity for higher BW devices.

## Slide 7: Comparison

## Slide 8: LPWAN Topologys
Star Topology
  No need for wireless network routing protocols
Direct Connection:

## Slide 9: LPWAN Topologies
Indirect Device connection:
  Devies connected to gateway using BLE/Zigbee.
Gateway typically mains powered
Can provide greater security at gateway

## Slide 10: Link Budget

## Slide 11: Use Cases – Smart Metering
Commodity consumption
No need for visits/concentrators

## Slide 12: Use Case – Utility Monitoring
Fire Hydrants
Portable Defoliators
Need to be sure they function when required

## Slide 13: Use Case - Tracking
Track location of goods/Equipment

## Slide 14: Use case - Agriculture
Monitor livestock and envornment

## Slide 15: Use Case – “Silver Economy”
Proactive Health monitoring

## Slide 16: LPWAN Technologies
Sigfox
  proprietary technology
  communication using the Industrial, Scientific and Medical ISM radio band
  868MHz in Europe and 902MHz in the US
LoRaWAN
  LoRa alliance is an open, non-profit association of members.
  intended for wireless battery operated Things in a regional, national or global network.

## Slide 17: SigFox Introduction
Market leader
One network
  No roaming
Nearly full coverage in Ireland/France and large parts of Europe
Open hardware approach
  Sell access to service

## Slide 18: Range
Best case scenario
100km line of sight
Typical
Few kms (city) to 10s kms (country)

## Slide 19: Outdoor and Indoor
Good Indoor propagation
  We’ll find out…
There will be signal attenuation

## Slide 20: Messages
Payload up to 12 bytes
Up to 140 times each day from a device (About 100b/s)
Devices can receive data from application