## Slide 1: Messaging for IoT (MQTT)
Frank Walsh

## Slide 2: HTTP
HTTP is a key protocol for distributed/web applications.
  Simple request/response model
  Supports REST
Excellent protocol for requesting data from a known source
Internet of Things has some extra requirements
  Emitting data from one thing to many
  Event-orientated – reacting to events when they happen.
  Large volumes of small data
  Constrained devices/things.
  Unreliable infrastructure

## Slide 3: Mobile Comms
Issues with
  data charges
  Power consumption
  Security
  Reliability (unreliable connections)
  Scalability

## Slide 4: Messaging Requirements for IoT
Lightweight for constrained devices
  Low bandwidth
  Low code base and computational footprint
Scalable
Reliable
Open accepted standard
Interoperable

## Slide 5: MQTT
MQ Telemetry Transport (MQTT)
Telemetry
  Remote measurements
Created by IBM
  from message queueing (MQ) architecture used by IBM for service oriented networks.
  There are no queues in MQTT.
Telemetry data goes from devices to a server or broker.
  Uses a publish/subscribe mechanism.
Lightweight both in bandwidth and code footprint

## Slide 6: MQTT is Open Source
Lots of implementations:
    Mosquitto
    Micro broker
    Really small message broker (RSMB): C
    Cloud services

## Slide 7: MQTT – publish subscribe
Topics/Subscriptions: Messages are published to topics.
  Clients can subscribe to a topic or a set of related topics
Publish/Subscribe: Clients can subscribe to topics or publish to topics.

## Slide 8: Publish Subscribe
A Publish Subscribe messaging protocol allowing a message to be published once
Many things can receive the message
The messaging service, or “broker”, provides decoupling between the producer and consumer(s)
A producer sends (publishes) a message (publication) on a topic (subject)
A consumer subscribes (makes a subscription) for messages on a topic (subject)
A message server / broker matches publications to subscriptions
  If no matches the message is discarded
  If one or more matches the message is delivered to each matching subscriber/consumer

## Slide 9: Publish Subscribe characteristics
A published messages may be retained
  A publisher can mark a message as “retained”
  The broker / server remembers the last known good message of a retained topic
  The broker / server gives the last known good message to new subscribers
A Subscription can be durable or non-durable
  Durable: messages forwarded to subscriber immediately, If subscriber not connected, message is stored and forwarded when connected
  Non-Durable: subscription only active when subscriber is connected to the server / broker

## Slide 10: MQTT Characteristics
MQTT protocol compresses to small number of bytes
  Smallest packet size 2 bytes
  Supports always-connected and sometimes connected
  Provides Session awareness
    Configurable keep alive providing granular session awareness
    “Last will and testament” enable applications to know when a client goes offline abnormally
    Typically utilises TCP based networks e.g. Webscokets
    Tested on many networks – vsat, gprs, 2G….

## Slide 11: MQTT Characteristics
Three quality of service levels:
  0 = At most once (Best effort, No Ack),
  1 = At least once (Acked, retransmitted if ack not received),
  2 = Exactly once [Request to send (Publish), Clear-to-send(Pubrec), message (Pubrel), ack (Pubcomp)]
Retained Messages
  Server keeps messages even after sending it to all subscribers. New subscribers get the retained messages

## Slide 12: MQTT vs HTTP
Push delivery of messages / data / events
  MQTT – low latency push delivery of messages from client to server and server to client. Helps bring an event oriented architecture to the web
  HTTP – push from client to server but poll from server to client
Efficient use of network
  For an M2M project the number of bytes with MQTT was 137130 bytes per device per month
  with HTTP the number of bytes was 801000 bytes per device per month
Reliable delivery over fragile network
  MQTT will deliver message to QOS even across connection breaks
  Decoupling and publish subscribe – one to many delivery

## Slide 13: Application Example
Home care monitoring solution
  Home and patient instrumented with sensors.
    E.g. door motion, blood pressure, pacemaker/defib.
  Collected by monitoring service (broker) using MQTT
  Subscribed by a health care service in the hospital
  Alerts relations/health care profs. if anything is out-of-order